## Slide 1: Previously On...
Voltage, Current and Resistance

## Slide 2: Ohm’s Law

## Slide 3: Previously On...
Voltage, Current and Resistance

## Slide 4: Previously On...
Voltage, Current and Resistance
Inputs and Outputs

## Slide 5: Previously On...
Voltage, Current and Resistance
Inputs and Outputs
Digital Vs. Analog

## Slide 6: Previously On...
Voltage, Current and Resistance
Inputs and Outputs
Digital Vs. Analog
Commands

## Slide 7: Previously On...
Voltage, Current and Resistance
Inputs and Outputs
Digital Vs. Analog
Commands
  pinMode(pin, INPUT/OUTPUT);
  digitalWrite(pin, HIGH/LOW);
  delay(ms);
  analogWrite(pin, 0-255);

## Slide 8: Previously On...
Voltage, Current and Resistance
Inputs and Outputs
Digital Vs. Analog
Commands
  pinMode(pin, INPUT/OUTPUT);
  digitalWrite(pin, HIGH/LOW);
  delay(ms);
  analogWrite(pin, 0-255);
Functions

## Slide 9: Previously On...
Voltage, Current and Resistance
Inputs and Outputs
Digital Vs. Analog
Commands
  pinMode(pin, INPUT/OUTPUT);
  digitalWrite(pin, HIGH/LOW);
  delay(ms);
  analogWrite(pin, 0-255);
Functions
  void setup() {}
  void loop() {}

## Slide 10: Previously On...
Voltage, Current and Resistance
Inputs and Outputs
Digital Vs. Analog
Commands
  pinMode(pin, INPUT/OUTPUT);
  digitalWrite(pin, HIGH/LOW);
  delay(ms);
  analogWrite(pin, 0-255);
Functions
  void setup() {}
  void loop() {}
Comments
  // Keep things clear

## Slide 11: Previously On...
Voltage, Current and Resistance
Inputs and Outputs
Digital Vs. Analog
Commands
  pinMode(pin, INPUT/OUTPUT);
  digitalWrite(pin, HIGH/LOW);
  delay(ms);
  analogWrite(pin, 0-255);
Functions
  void setup() {}
  void loop() {}
Comments
  // Keep things clear
Variables
  int led = 9;
  int brightness = brightness + 1;

## Slide 12: The Most Important Lesson
Notes: This is why there’s a diversity problem in Engineering

## Slide 13: Inputs!
Input is any signal entering an electrical system
Both digital and analog sensors are forms of input
Input can also take many other forms: a keyboard, a mouse, infrared sensors, biometric sensors, touch sensors, cameras or just plain voltage from a circuit
This is how you can make a computer react to the world around it

## Slide 14: Digital Input
Like digital output, can only sense if a signal is high or low
For Arduino
  High is voltage above 3 V
  Low is voltage below 1.5 V
General category is “switches”
Includes push buttons (momentary switches), toggle switches, knife switches (maintained switches), capacitive/touch switches, and many other sensors

## Slide 15: Component Spotlight: The Push Button / Momentary Switch

## Slide 16: Push Button and Breadboard Connections
Our buttons have to bridge the gap on our breadboards
The top pins are connected to each other and so are the bottom ones

## Slide 17: Using the Breadboard to Built a Simple Input Circuit
Remember our original circuit?

## Slide 18: Using the Breadboard to Built a Simple Input Circuit
Remember our original circuit?
We’re going to wire that up again, but this time with a switch

## Slide 19: Using the Breadboard to Built a Simple Input Circuit

## Slide 20: Go ahead and plug your board in!

## Slide 21: Adding Control

## Slide 22: Adding Control
Any circuit that has meaningful input has some degree of control

## Slide 23: Adding Control
Any circuit that has meaningful input has some degree of control
Microcontrollers allow us to assign different relationships between inputs and outputs

## Slide 24
if() statements / Boolean logic
Project #3 – Lie Detector
Just give me 3 clock cycles with the perp...
Psuedo-code – how should this work?
Statement true?
NO
YES
Green LED turns on
Red LED turns on

## Slide 25: Project #3 – Lie Detector Inputs and Outputs
Statement true?
NO
YES
Green LED turns on
Red LED turns on
Inputs | Outputs
None | Green LED
 | Red LED
Notes: Our program is running hundreds of thousands of times every second

## Slide 26: Project #3 – Lie Detector Schematic
You can leave the button on the breadboard- we’ll be using it again soon

## Slide 27: Project #3 – Lie Detector Wiring Diagram

## Slide 28: Project #3 – Lie Detector Conditional Statements
the if() statement

## Slide 29: Project #3 – Lie Detector Conditional Statements
If this is true

## Slide 30: Project #3 – Lie Detector Conditional Statements
If this is true
Do this

## Slide 31: Project #3 – Lie Detector Conditional Statements
If this is true
Do this
Otherwise

## Slide 32: Project #3 – Lie Detector Conditional Statements
If this is true
Do this
Otherwise
Do this

## Slide 33: Boolean Operators
<Boolean> | True if:
(a) | a is true, HIGH or does not equal zero
(!a) | a is false, LOW or equals zero
(a) == (b) | a is equal to b
(a) != (b) | a is not equal to b
(a) > (b) | a is greater than b
(a) >= (b) | a is greater than or equal to b
(a) < (b) | a is less than b
(a) <= (b) | a is less than or equal to b
(a) && (b) | both a is true AND b is true
(a) ¦¦ (b) | either a is true OR b is true

## Slide 34: Déjà Vu

## Slide 35: Project #3 – Lie Detector Code Review
1 | /*
2 | * Test our if() statements
3 | */
4 | 
5 | // assign pin based off circuit
6 | int red_led = 13;
7 | int green_led = 12;
8 | 
9 | // these are the variables we'll play around with
10 | int a = true;
11 | int b = false;
12 | 
13 | // the setup function runs once when you press reset or power the board
14 | void setup() {
15 | pinMode(red_led, OUTPUT);
16 | pinMode(green_led, OUTPUT);
17 | 
18 | // change the expression inside the if() and look at the results
19 | if (a) {
20 | digitalWrite(red_led, LOW);
21 | digitalWrite(green_led, HIGH);
22 | }
23 | else {
24 | digitalWrite(green_led, LOW);
25 | digitalWrite(red_led, HIGH);
26 | }
27 | }
28 | 
29 | // the loop function runs over and over again forever
30 | void loop() {
31 | 
32 | }

## Slide 36: Project #3 – Lie Detector Code Review
1 | /*
2 | * Test our if() statements
3 | */
4 | 
5 | // assign pin based off circuit
6 | int red_led = 13;
7 | int green_led = 12;
8 | 
9 | // these are the variables we'll play around with
10 | int a = true;
11 | int b = false;
12 | 
13 | // the setup function runs once when you press reset or power the board
14 | void setup() {
15 | pinMode(red_led, OUTPUT);
16 | pinMode(green_led, OUTPUT);
17 | 
18 | // change the expression inside the if() and look at the results
19 | if (b) {
20 | digitalWrite(red_led, LOW);
21 | digitalWrite(green_led, HIGH);
22 | }
23 | else {
24 | digitalWrite(green_led, LOW);
25 | digitalWrite(red_led, HIGH);
26 | }
27 | }
28 | 
29 | // the loop function runs over and over again forever
30 | void loop() {
31 | 
32 | }

## Slide 37: Project #3 – Lie Detector Code Review
1 | /*
2 | * Test our if() statements
3 | */
4 | 
5 | // assign pin based off circuit
6 | int red_led = 13;
7 | int green_led = 12;
8 | 
9 | // these are the variables we'll play around with
10 | int a = true;
11 | int b = false;
12 | 
13 | // the setup function runs once when you press reset or power the board
14 | void setup() {
15 | pinMode(red_led, OUTPUT);
16 | pinMode(green_led, OUTPUT);
17 | 
18 | // change the expression inside the if() and look at the results
19 | if (!b) {
20 | digitalWrite(red_led, LOW);
21 | digitalWrite(green_led, HIGH);
22 | }
23 | else {
24 | digitalWrite(green_led, LOW);
25 | digitalWrite(red_led, HIGH);
26 | }
27 | }
28 | 
29 | // the loop function runs over and over again forever
30 | void loop() {
31 | 
32 | }

## Slide 38: Project #3 – Lie Detector Code Review
1 | /*
2 | * Test our if() statements
3 | */
4 | 
5 | // assign pin based off circuit
6 | int red_led = 13;
7 | int green_led = 12;
8 | 
9 | // these are the variables we'll play around with
10 | int a = true;
11 | int b = false;
12 | 
13 | // the setup function runs once when you press reset or power the board
14 | void setup() {
15 | pinMode(red_led, OUTPUT);
16 | pinMode(green_led, OUTPUT);
17 | 
18 | // change the expression inside the if() and look at the results
19 | if (!a) {
20 | digitalWrite(red_led, LOW);
21 | digitalWrite(green_led, HIGH);
22 | }
23 | else {
24 | digitalWrite(green_led, LOW);
25 | digitalWrite(red_led, HIGH);
26 | }
27 | }
28 | 
29 | // the loop function runs over and over again forever
30 | void loop() {
31 | 
32 | }

## Slide 39: Project #3 – Lie Detector Code Review
1 | /*
2 | * Test our if() statements
3 | */
4 | 
5 | // assign pin based off circuit
6 | int red_led = 13;
7 | int green_led = 12;
8 | 
9 | // these are the variables we'll play around with
10 | int a = 9;
11 | int b = 5;
12 | 
13 | // the setup function runs once when you press reset or power the board
14 | void setup() {
15 | pinMode(red_led, OUTPUT);
16 | pinMode(green_led, OUTPUT);
17 | 
18 | // change the expression inside the if() and look at the results
19 | if (a > b) {
20 | digitalWrite(red_led, LOW);
21 | digitalWrite(green_led, HIGH);
22 | }
23 | else {
24 | digitalWrite(green_led, LOW);
25 | digitalWrite(red_led, HIGH);
26 | }
27 | }
28 | 
29 | // the loop function runs over and over again forever
30 | void loop() {
31 | 
32 | }

## Slide 40: Project #3 – Lie Detector Code Review
1 | /*
2 | * Test our if() statements
3 | */
4 | 
5 | // assign pin based off circuit
6 | int red_led = 13;
7 | int green_led = 12;
8 | 
9 | // these are the variables we'll play around with
10 | int a = 9;
11 | int b = 5;
12 | 
13 | // the setup function runs once when you press reset or power the board
14 | void setup() {
15 | pinMode(red_led, OUTPUT);
16 | pinMode(green_led, OUTPUT);
17 | 
18 | // change the expression inside the if() and look at the results
19 | if (a < b) {
20 | digitalWrite(red_led, LOW);
21 | digitalWrite(green_led, HIGH);
22 | }
23 | else {
24 | digitalWrite(green_led, LOW);
25 | digitalWrite(red_led, HIGH);
26 | }
27 | }
28 | 
29 | // the loop function runs over and over again forever
30 | void loop() {
31 | 
32 | }

## Slide 41: Project #3 – Lie Detector Code Review
1 | /*
2 | * Test our if() statements
3 | */
4 | 
5 | // assign pin based off circuit
6 | int red_led = 13;
7 | int green_led = 12;
8 | 
9 | // these are the variables we'll play around with
10 | int a = true;
11 | int b = 5;
12 | 
13 | // the setup function runs once when you press reset or power the board
14 | void setup() {
15 | pinMode(red_led, OUTPUT);
16 | pinMode(green_led, OUTPUT);
17 | 
18 | // change the expression inside the if() and look at the results
19 | if (b > 5 ¦¦ a) {
20 | digitalWrite(red_led, LOW);
21 | digitalWrite(green_led, HIGH);
22 | }
23 | else {
24 | digitalWrite(green_led, LOW);
25 | digitalWrite(red_led, HIGH);
26 | }
27 | }
28 | 
29 | // the loop function runs over and over again forever
30 | void loop() {
31 | 
32 | }

## Slide 42: Project #3 – Lie Detector Code Review
1 | /*
2 | * Test our if() statements
3 | */
4 | 
5 | // assign pin based off circuit
6 | int red_led = 13;
7 | int green_led = 12;
8 | 
9 | // these are the variables we'll play around with
10 | int a = true;
11 | int b = 5;
12 | 
13 | // the setup function runs once when you press reset or power the board
14 | void setup() {
15 | pinMode(red_led, OUTPUT);
16 | pinMode(green_led, OUTPUT);
17 | 
18 | // change the expression inside the if() and look at the results
19 | if (b > 5 && a) {
20 | digitalWrite(red_led, LOW);
21 | digitalWrite(green_led, HIGH);
22 | }
23 | else {
24 | digitalWrite(green_led, LOW);
25 | digitalWrite(red_led, HIGH);
26 | }
27 | }
28 | 
29 | // the loop function runs over and over again forever
30 | void loop() {
31 | 
32 | }

## Slide 43: Project #3 – Lie Detector Code Review
1 | /*
2 | * Test our if() statements
3 | */
4 | 
5 | // assign pin based off circuit
6 | int red_led = 13;
7 | int green_led = 12;
8 | 
9 | // these are the variables we'll play around with
10 | int a = true;
11 | int b = 5;
12 | 
13 | // the setup function runs once when you press reset or power the board
14 | void setup() {
15 | pinMode(red_led, OUTPUT);
16 | pinMode(green_led, OUTPUT);
17 | 
18 | // change the expression inside the if() and look at the results
19 | if (b >= 5 && a) {
20 | digitalWrite(red_led, LOW);
21 | digitalWrite(green_led, HIGH);
22 | }
23 | else {
24 | digitalWrite(green_led, LOW);
25 | digitalWrite(red_led, HIGH);
26 | }
27 | }
28 | 
29 | // the loop function runs over and over again forever
30 | void loop() {
31 | 
32 | }

## Slide 44: Boolean Operators
<Boolean> | True if:
(a) | a is true, HIGH or does not equal zero
(!a) | a is false, LOW or equals zero
(a) == (b) | a is equal to b
(a) != (b) | a is not equal to b
(a) > (b) | a is greater than b
(a) >= (b) | a is greater than or equal to b
(a) < (b) | a is less than b
(a) <= (b) | a is less than or equal to b
(a) && (b) | both a is true AND b is true
(a) ¦¦ (b) | either a is true OR b is true

## Slide 45
Project #4 – Button/Maintained Switch Switch
Who you callin’ momentary?
Psuedo-code – how should this work?
digitalRead()
Button Pressed?
YES
LED
status?
OFF
ON
LED turns off
Rinse & Repeat
LED turns on

## Slide 46
Project #4 – Button/Maintained Switch Switch
Who you callin’ momentary?
Psuedo-code – how should this work?
digitalRead()
Button Pressed?
YES
LED
status?
OFF
ON
LED turns off
Rinse & Repeat
LED turns on
Pressed Before?
NO

## Slide 47: Project #4 – Button/Maintained Switch Switch Inputs and Outputs
Button Pressed?
YES
LED
status?
OFF
ON
LED turns off
Rinse & Repeat
LED turns on
Pressed Before?
NO
Inputs | Outputs
Push Button | LED
Notes: Our program is running hundreds of thousands of times every second

## Slide 48: Transitioning to Micro-control Output & Input

## Slide 49: Transitioning to Micro-control Output & Input

## Slide 50: Project #4 – Button/Maintained Switch Switch Wiring Diagram

## Slide 51: Project #4 – Button/Maintained Switch Switch Wiring Diagram
WRONG!!!

## Slide 52: This Part Is Good

## Slide 53: So This Must Be Bad…

## Slide 54: So This Must Be Bad… But Why?!

## Slide 55: Another Water Analogy

## Slide 56: Analogy Continued...

## Slide 57: Analogy Continued...
?

## Slide 58: All Stopped Up

## Slide 59: All Stopped Up (kinda)

## Slide 60: Switch Off

## Slide 61: Switch On

## Slide 62: Switch Off?!

## Slide 63: Analogy Extended (Thin but holding)

## Slide 64: So This Approach...

## Slide 65: Doesn’t Work!

## Slide 66: What About...

## Slide 67: Changing Bathroom Fixtures?

## Slide 69: Getting Rid of the Unnecessary Crap

## Slide 70: Changing the Viewpoint

## Slide 71: Changing the Viewpoint

## Slide 72: Changing the Viewpoint

## Slide 73: Changing the Viewpoint

## Slide 74: Switch Off

## Slide 75: Switch On

## Slide 76: Switch Right After Off

## Slide 77: Switch Off

## Slide 78: Stop Playin’ With the Commode!!

## Slide 79: Possible Solution

## Slide 80: How Do We Get Here?
?

## Slide 81: Resistance Analogy
Big Pipe == Lower Resistance
Small Pipe == Higher Resistance
Water
Tower
Water
Tower
V

## Slide 82: How Do We Get Here?
?

## Slide 83: The Pull-Up Resistor!

## Slide 84: But There’s A Trade-Off Between This...

## Slide 85: …And This

## Slide 86: It’s All About Compromise
10kΩ is a good value
(brown-black-black-red-gold)
or
(brown-black-orange-gold)

## Slide 87: Decoding Resistor Values

## Slide 88: Project #4 – Button/Maintained Switch Switch Input Schematic
Schematic of Pull-Up Resistor and Switch

## Slide 89: Project #4 – Button/Maintained Switch Switch Full Schematic
And the output is still the same as Project 1!

## Slide 90: Project #4 – Button/Maintained Switch Switch Wiring Diagram

## Slide 91: Project #4 – Button/Maintained Switch Switch Our First Input Commands!
pinMode(pin, INPUT/OUTPUT);
Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.

## Slide 92: Project #4 – Button/Maintained Switch Switch Our First Input Commands!
pinMode(pin, INPUT/OUTPUT);
ex: pinMode(2, INPUT);
Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.

## Slide 93: Project #4 – Button/Maintained Switch Switch Our First Input Commands!
pinMode(pin, INPUT/OUTPUT);
ex: pinMode(2, INPUT);
digitalRead(pin);
Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.

## Slide 94: Project #4 – Button/Maintained Switch Switch Our First Input Commands!
pinMode(pin, INPUT/OUTPUT);
ex: pinMode(2, INPUT);
digitalRead(pin);
ex: digitalRead(2);
Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.

## Slide 95: Project #4 – Button/Maintained Switch Switch Our First Input Commands!
pinMode(pin, INPUT/OUTPUT);
ex: pinMode(2, INPUT);
digitalRead(pin);
ex: digitalRead(2);
ex: int button_state = digitalRead(2);
Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.

## Slide 96: Project #4 – Button/Maintained Switch Switch Our First Input Commands!
pinMode(pin, INPUT/OUTPUT);
ex: pinMode(2, INPUT);
digitalRead(pin);
ex: digitalRead(2);
ex: int button_state = digitalRead(2);
button_state will either be HIGH or LOW
HIGH if switch is off, LOW if switch is on
Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.

## Slide 97: Project #4 – Button/Maintained Switch Switch Code Review

## Slide 98: Code Review Continued

## Slide 99: Code Review Continued

## Slide 100: Project #4 – Button/Maintained Switch Switch Puzzles
Challenge 4a – Wire another LED. Make the button turn one off and the other on
Challenge 4b – Make an LED blink when you press the button (hint: look at File>Examples>Digital>Blink Without Delay)
Challenge 4c – Make an LED alternate between off, on and blink by pressing the button

## Slide 102: Special Thanks:
www.sparkfun.com
6175 Longbow Drive, Suite 200
Boulder, Colorado 80301