## Slide 1: Previously On...
Voltage, Current and Resistance
Inputs and Outputs
Digital Vs. Analog
Commands
  pinMode(pin, INPUT/OUTPUT);
  digitalWrite(pin, HIGH/LOW);
  delay(ms);
  analogWrite(pin, 0-255);
Functions
  void setup() {}
  void loop() {}
Comments
  // Keep things clear
Variables
  int led = 9;
  int brightness = brightness + 1;

## Slide 2: Ohm’s Law

## Slide 3: Previously On...
Voltage, Current and Resistance
Inputs and Outputs
Digital Vs. Analog
Commands
  pinMode(pin, INPUT/OUTPUT);
  digitalWrite(pin, HIGH/LOW);
  delay(ms);
  analogWrite(pin, 0-255);
Functions
  void setup() {}
  void loop() {}
Comments
  // Keep things clear
Variables
  int led = 9;
  int brightness = brightness + 1;

## Slide 4: The Most Important Lesson
Notes: This is why there’s a diversity problem in Engineering

## Slide 5: Inputs!
Input is any signal entering an electrical system
Both digital and analog sensors are forms of input
Input can also take many other forms: a keyboard, a mouse, infrared sensors, biometric sensors, touch sensors or just plain voltage from a circuit
This is what makes interactive exhibits interactive

## Slide 6: Digital Input
Like digital output, can only sense if a signal is high or low
For Arduino
  High is voltage above 3 V
  Low is voltage below 1.5 V
General category is “switches”
Includes push buttons (momentary switches), toggle switches, knife switches (maintained switches), capacitive/touch switches, and many other sensors

## Slide 7: Component Spotlight: The Push Button / Momentary Switch

## Slide 8: Push Button and Breadboard Connections
Our buttons have to bridge the gap on our breadboards
The top pins are connected to each other and so are the bottom ones

## Slide 9: Using the Breadboard to Built a Simple Input Circuit
Remember our original circuit?

## Slide 10: Using the Breadboard to Built a Simple Input Circuit
Remember our original circuit?
We’re going to wire that up again, but this time with a switch

## Slide 11: Using the Breadboard to Built a Simple Input Circuit

## Slide 12: Using the Breadboard to Built a Simple Input Circuit

## Slide 13: Go ahead and plug your board in!

## Slide 14: Adding Control

## Slide 15: Adding Control
Any circuit that has meaningful input has some degree of control

## Slide 16: Adding Control
Any circuit that has meaningful input has some degree of control
Microcontrollers allow us to assign different relationships between inputs and outputs

## Slide 17
if() statements / Boolean logic
Project #3 – Lie Detector
Just give me 3 clock cycles with the bastard
Psuedo-code – how should this work?
Statement true?
NO
YES
Green LED turns on
Red LED turns on

## Slide 18: Project #3 – Lie Detector Inputs and Outputs
Statement true?
NO
YES
Green LED turns on
Red LED turns on
Inputs | Outputs
None | Green LED
 | Red LED
Notes: Our program is running hundreds of thousands of times every second

## Slide 19: Project #3 – Lie Detector Schematic
You can leave the button on the breadboard- we’ll be using it again soon

## Slide 20: Project #3 – Lie Detector Wiring Diagram

## Slide 21: Project #3 – Lie Detector Conditional Statements
the if() statement

## Slide 22: Project #3 – Lie Detector Conditional Statements
If this is true

## Slide 23: Project #3 – Lie Detector Conditional Statements
If this is true
Do this

## Slide 24: Project #3 – Lie Detector Conditional Statements
If this is true
Do this
Otherwise

## Slide 25: Project #3 – Lie Detector Conditional Statements
If this is true
Do this
Otherwise
Do this

## Slide 26: Boolean Operators
<Boolean> | True if:
(a) | a is true, HIGH or does not equal zero
(!a) | a is false, LOW or equals zero
(a) == (b) | a is equal to b
(a) != (b) | a is not equal to b
(a) > (b) | a is greater than b
(a) >= (b) | a is greater than or equal to b
(a) < (b) | a is less than b
(a) <= (b) | a is less than or equal to b
(a) && (b) | both a is true AND b is true
(a) ¦¦ (b) | either a is true OR b is true

## Slide 27: Déjà Vu

## Slide 28: Project #3 – Lie Detector Code Review
1 | /*
2 | * Test our if() statements
3 | */
4 | 
5 | // assign pin based off circuit
6 | int red_led = 13;
7 | int green_led = 12;
8 | 
9 | // these are the variables we'll play around with
10 | int a = true;
11 | int b = false;
12 | 
13 | // the setup function runs once when you press reset or power the board
14 | void setup() {
15 | pinMode(red_led, OUTPUT);
16 | pinMode(green_led, OUTPUT);
17 | 
18 | // change the expression inside the if() and look at the results
19 | if (a) {
20 | digitalWrite(red_led, LOW);
21 | digitalWrite(green_led, HIGH);
22 | }
23 | else {
24 | digitalWrite(green_led, LOW);
25 | digitalWrite(red_led, HIGH);
26 | }
27 | }
28 | 
29 | // the loop function runs over and over again forever
30 | void loop() {
31 | 
32 | }

## Slide 29: Project #3 – Lie Detector Code Review
1 | /*
2 | * Test our if() statements
3 | */
4 | 
5 | // assign pin based off circuit
6 | int red_led = 13;
7 | int green_led = 12;
8 | 
9 | // these are the variables we'll play around with
10 | int a = true;
11 | int b = false;
12 | 
13 | // the setup function runs once when you press reset or power the board
14 | void setup() {
15 | pinMode(red_led, OUTPUT);
16 | pinMode(green_led, OUTPUT);
17 | 
18 | // change the expression inside the if() and look at the results
19 | if (b) {
20 | digitalWrite(red_led, LOW);
21 | digitalWrite(green_led, HIGH);
22 | }
23 | else {
24 | digitalWrite(green_led, LOW);
25 | digitalWrite(red_led, HIGH);
26 | }
27 | }
28 | 
29 | // the loop function runs over and over again forever
30 | void loop() {
31 | 
32 | }

## Slide 30: Project #3 – Lie Detector Code Review
1 | /*
2 | * Test our if() statements
3 | */
4 | 
5 | // assign pin based off circuit
6 | int red_led = 13;
7 | int green_led = 12;
8 | 
9 | // these are the variables we'll play around with
10 | int a = true;
11 | int b = false;
12 | 
13 | // the setup function runs once when you press reset or power the board
14 | void setup() {
15 | pinMode(red_led, OUTPUT);
16 | pinMode(green_led, OUTPUT);
17 | 
18 | // change the expression inside the if() and look at the results
19 | if (!b) {
20 | digitalWrite(red_led, LOW);
21 | digitalWrite(green_led, HIGH);
22 | }
23 | else {
24 | digitalWrite(green_led, LOW);
25 | digitalWrite(red_led, HIGH);
26 | }
27 | }
28 | 
29 | // the loop function runs over and over again forever
30 | void loop() {
31 | 
32 | }

## Slide 31: Project #3 – Lie Detector Code Review
1 | /*
2 | * Test our if() statements
3 | */
4 | 
5 | // assign pin based off circuit
6 | int red_led = 13;
7 | int green_led = 12;
8 | 
9 | // these are the variables we'll play around with
10 | int a = true;
11 | int b = false;
12 | 
13 | // the setup function runs once when you press reset or power the board
14 | void setup() {
15 | pinMode(red_led, OUTPUT);
16 | pinMode(green_led, OUTPUT);
17 | 
18 | // change the expression inside the if() and look at the results
19 | if (!a) {
20 | digitalWrite(red_led, LOW);
21 | digitalWrite(green_led, HIGH);
22 | }
23 | else {
24 | digitalWrite(green_led, LOW);
25 | digitalWrite(red_led, HIGH);
26 | }
27 | }
28 | 
29 | // the loop function runs over and over again forever
30 | void loop() {
31 | 
32 | }

## Slide 32: Project #3 – Lie Detector Code Review
1 | /*
2 | * Test our if() statements
3 | */
4 | 
5 | // assign pin based off circuit
6 | int red_led = 13;
7 | int green_led = 12;
8 | 
9 | // these are the variables we'll play around with
10 | int a = 9;
11 | int b = 5;
12 | 
13 | // the setup function runs once when you press reset or power the board
14 | void setup() {
15 | pinMode(red_led, OUTPUT);
16 | pinMode(green_led, OUTPUT);
17 | 
18 | // change the expression inside the if() and look at the results
19 | if (a > b) {
20 | digitalWrite(red_led, LOW);
21 | digitalWrite(green_led, HIGH);
22 | }
23 | else {
24 | digitalWrite(green_led, LOW);
25 | digitalWrite(red_led, HIGH);
26 | }
27 | }
28 | 
29 | // the loop function runs over and over again forever
30 | void loop() {
31 | 
32 | }

## Slide 33: Project #3 – Lie Detector Code Review
1 | /*
2 | * Test our if() statements
3 | */
4 | 
5 | // assign pin based off circuit
6 | int red_led = 13;
7 | int green_led = 12;
8 | 
9 | // these are the variables we'll play around with
10 | int a = 9;
11 | int b = 5;
12 | 
13 | // the setup function runs once when you press reset or power the board
14 | void setup() {
15 | pinMode(red_led, OUTPUT);
16 | pinMode(green_led, OUTPUT);
17 | 
18 | // change the expression inside the if() and look at the results
19 | if (a < b) {
20 | digitalWrite(red_led, LOW);
21 | digitalWrite(green_led, HIGH);
22 | }
23 | else {
24 | digitalWrite(green_led, LOW);
25 | digitalWrite(red_led, HIGH);
26 | }
27 | }
28 | 
29 | // the loop function runs over and over again forever
30 | void loop() {
31 | 
32 | }

## Slide 34: Project #3 – Lie Detector Code Review
1 | /*
2 | * Test our if() statements
3 | */
4 | 
5 | // assign pin based off circuit
6 | int red_led = 13;
7 | int green_led = 12;
8 | 
9 | // these are the variables we'll play around with
10 | int a = true;
11 | int b = 5;
12 | 
13 | // the setup function runs once when you press reset or power the board
14 | void setup() {
15 | pinMode(red_led, OUTPUT);
16 | pinMode(green_led, OUTPUT);
17 | 
18 | // change the expression inside the if() and look at the results
19 | if (b > 5 ¦¦ a) {
20 | digitalWrite(red_led, LOW);
21 | digitalWrite(green_led, HIGH);
22 | }
23 | else {
24 | digitalWrite(green_led, LOW);
25 | digitalWrite(red_led, HIGH);
26 | }
27 | }
28 | 
29 | // the loop function runs over and over again forever
30 | void loop() {
31 | 
32 | }

## Slide 35: Project #3 – Lie Detector Code Review
1 | /*
2 | * Test our if() statements
3 | */
4 | 
5 | // assign pin based off circuit
6 | int red_led = 13;
7 | int green_led = 12;
8 | 
9 | // these are the variables we'll play around with
10 | int a = true;
11 | int b = 5;
12 | 
13 | // the setup function runs once when you press reset or power the board
14 | void setup() {
15 | pinMode(red_led, OUTPUT);
16 | pinMode(green_led, OUTPUT);
17 | 
18 | // change the expression inside the if() and look at the results
19 | if (b > 5 && a) {
20 | digitalWrite(red_led, LOW);
21 | digitalWrite(green_led, HIGH);
22 | }
23 | else {
24 | digitalWrite(green_led, LOW);
25 | digitalWrite(red_led, HIGH);
26 | }
27 | }
28 | 
29 | // the loop function runs over and over again forever
30 | void loop() {
31 | 
32 | }

## Slide 36: Project #3 – Lie Detector Code Review
1 | /*
2 | * Test our if() statements
3 | */
4 | 
5 | // assign pin based off circuit
6 | int red_led = 13;
7 | int green_led = 12;
8 | 
9 | // these are the variables we'll play around with
10 | int a = true;
11 | int b = 5;
12 | 
13 | // the setup function runs once when you press reset or power the board
14 | void setup() {
15 | pinMode(red_led, OUTPUT);
16 | pinMode(green_led, OUTPUT);
17 | 
18 | // change the expression inside the if() and look at the results
19 | if (b >= 5 && a) {
20 | digitalWrite(red_led, LOW);
21 | digitalWrite(green_led, HIGH);
22 | }
23 | else {
24 | digitalWrite(green_led, LOW);
25 | digitalWrite(red_led, HIGH);
26 | }
27 | }
28 | 
29 | // the loop function runs over and over again forever
30 | void loop() {
31 | 
32 | }

## Slide 37: Boolean Operators
<Boolean> | True if:
(a) | a is true, HIGH or does not equal zero
(!a) | a is false, LOW or equals zero
(a) == (b) | a is equal to b
(a) != (b) | a is not equal to b
(a) > (b) | a is greater than b
(a) >= (b) | a is greater than or equal to b
(a) < (b) | a is less than b
(a) <= (b) | a is less than or equal to b
(a) && (b) | both a is true AND b is true
(a) ¦¦ (b) | either a is true OR b is true

## Slide 38
Project #4 – Button/Maintained Switch Switch
Who you callin’ momentary?
Psuedo-code – how should this work?
digitalRead()
Button Pressed?
YES
LED
status?
OFF
ON
LED turns off
Rinse & Repeat
LED turns on

## Slide 39
Project #4 – Button/Maintained Switch Switch
Who you callin’ momentary?
Psuedo-code – how should this work?
digitalRead()
Button Pressed?
YES
LED
status?
OFF
ON
LED turns off
Rinse & Repeat
LED turns on
Pressed Before?
NO

## Slide 40: Project #4 – Button/Maintained Switch Switch Inputs and Outputs
Button Pressed?
YES
LED
status?
OFF
ON
LED turns off
Rinse & Repeat
LED turns on
Pressed Before?
NO
Inputs | Outputs
Push Button | LED
Notes: Our program is running hundreds of thousands of times every second

## Slide 41: Transitioning to Micro-control Output & Input

## Slide 42: Transitioning to Micro-control Output & Input

## Slide 43: Project #4 – Button/Maintained Switch Switch Wiring Diagram

## Slide 44: Project #4 – Button/Maintained Switch Switch Wiring Diagram
WRONG!!!

## Slide 45: This Part Is Good

## Slide 46: So This Must Be Bad…

## Slide 47: So This Must Be Bad… But Why?!

## Slide 48: Another Water Analogy

## Slide 49: Analogy Continued...

## Slide 50: Analogy Continued...
?

## Slide 51: All Stopped Up

## Slide 52: All Stopped Up (kinda)

## Slide 53: Switch Off

## Slide 54: Switch On

## Slide 55: Switch Off?!

## Slide 56: Analogy Extended (Thin but holding)

## Slide 57: So This Approach...

## Slide 58: Doesn’t Work!

## Slide 59: What About...

## Slide 60: Changing Bathroom Fixtures?

## Slide 62: Getting Rid of the Unnecessary Crap

## Slide 63: Changing the Viewpoint

## Slide 64: Changing the Viewpoint

## Slide 65: Changing the Viewpoint

## Slide 66: Changing the Viewpoint

## Slide 67: Switch Off

## Slide 68: Switch On

## Slide 69: Switch Right After Off

## Slide 70: Switch Off

## Slide 71: Stop Playin’ With the Commode!!

## Slide 72: Possible Solution

## Slide 73: How Do We Get Here?
?

## Slide 74: Resistance Analogy
Big Pipe == Lower Resistance
Small Pipe == Higher Resistance
Water
Tower
Water
Tower
V

## Slide 75: How Do We Get Here?
?

## Slide 76: The Pull-Up Resistor!

## Slide 77: But There’s A Trade-Off Between This...

## Slide 78: …And This

## Slide 79: It’s All About Compromise
10kΩ is a good value
(brown-black-black-red-gold)
or
(brown-black-orange-gold)

## Slide 80: Decoding Resistor Values

## Slide 81: Project #4 – Button/Maintained Switch Switch Input Schematic
Schematic of Pull-Up Resistor and Switch

## Slide 82: Project #4 – Button/Maintained Switch Switch Full Schematic
And the output is still the same as Project 1!

## Slide 83: Project #4 – Button/Maintained Switch Switch Wiring Diagram

## Slide 84: Project #4 – Button/Maintained Switch Switch Our First Input Commands!
pinMode(pin, INPUT/OUTPUT);
Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.

## Slide 85: Project #4 – Button/Maintained Switch Switch Our First Input Commands!
pinMode(pin, INPUT/OUTPUT);
ex: pinMode(2, INPUT);
Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.

## Slide 86: Project #4 – Button/Maintained Switch Switch Our First Input Commands!
pinMode(pin, INPUT/OUTPUT);
ex: pinMode(2, INPUT);
digitalRead(pin);
Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.

## Slide 87: Project #4 – Button/Maintained Switch Switch Our First Input Commands!
pinMode(pin, INPUT/OUTPUT);
ex: pinMode(2, INPUT);
digitalRead(pin);
ex: digitalRead(2);
Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.

## Slide 88: Project #4 – Button/Maintained Switch Switch Our First Input Commands!
pinMode(pin, INPUT/OUTPUT);
ex: pinMode(2, INPUT);
digitalRead(pin);
ex: digitalRead(2);
ex: int button_state = digitalRead(2);
Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.

## Slide 89: Project #4 – Button/Maintained Switch Switch Our First Input Commands!
pinMode(pin, INPUT/OUTPUT);
ex: pinMode(2, INPUT);
digitalRead(pin);
ex: digitalRead(2);
ex: int button_state = digitalRead(2);
button_state will either be HIGH or LOW
HIGH if switch is off, LOW if switch is on
Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.

## Slide 90: Project #4 – Button/Maintained Switch Switch Code Review

## Slide 91: Code Review Continued

## Slide 92: Code Review Continued

## Slide 93: Project #4 – Button/Maintained Switch Switch Puzzles
Challenge 4a – Wire another LED. Make the button turn one off and the other on
Challenge 4b – Make an LED blink when you press the button (hint: look at File>Examples>Digital>Blink Without Delay)
Challenge 4c – Make an LED alternate between off, on and blink by pressing the button

## Slide 94
Project #4 – Night Light
How Dark Is Too Dark?
Psuedo-code – how should this work?
Check How Dark It Is
How Dark Is It?
IT’S FINE
TOO DARK!
LED turns on
Rinse & Repeat
LED turns off
analogRead()

## Slide 95: Project #4 - Night Light Inputs and Outputs
Check How Dark It Is
How Dark Is It?
IT’S FINE
TOO DARK!
LED turns on
Rinse & Repeat
LED turns off
Inputs | Outputs
Photoresistor | LED

## Slide 96: The Voltage Divider

## Slide 97: The Voltage Divider

## Slide 98: The Voltage Divider
“From each according to their ability, to each according to their need.”

## Slide 99: The Voltage Divider
How many carrots does the fairy have left at this point?

## Slide 100: The Voltage Divider
How many carrots does the fairy have left at this point?

## Slide 101: The Voltage Divider
How many carrots does the fairy have left at this point?

## Slide 102: The Voltage Divider
How many carrots does the fairy have left at this point?

## Slide 103: The Voltage Divider
How many carrots does the fairy have left at this point?

## Slide 104: The Switch-Over

## Slide 105: Project #4 – Night Light Schematic

## Slide 106: Project #4 – Night Light Wiring Diagram

## Slide 107: Project #4 – Night Light
int sensor_val = analogRead(pin);
pin – refers to the analog input pin (limited to pins A0, A1, A2, A3, A4 and A5)
Arduino uses a 10-bit analog-to-digital converter (ADC):
This means that sensor_val is always a number between 0 and 1023
  Minimum Carrots → 0
  Maximum Carrots → 1023

## Slide 108: Determining Analog Values
But the top bunny is always going to get some carrots, so we can’t really get to 1023
And we can’t really make our bottom bunny so small that it gets 0 carrots
So how do we determine the minimum and maximum numbers for our circuit?
Do math

## Slide 109: Determining Analog Values
But the top bunny is always going to get some carrots, so we can’t really get to 1023
And we can’t really make our bottom bunny so small that it gets 0 carrots
So how do we determine the minimum and maximum numbers for our circuit?
Do math
Ask the microcontroller

## Slide 110: Using Serial Communication
Method used to transfer data between two devices.
Arduino dedicates Digital I/O pin # 0 to receiving and Digital I/O pin #1 to transmit.
Data passes between the computer and Arduino through the Universal Serial Bus (USB!) cable. Data is transmitted as zeros (‘0’) and ones (‘1’) sequentially.
Notes: Serial is the same for novels, soldiers, murders, killers, communication
For this reason, we typically do not use Digital I/O 0 or 1 for anything in our designs.

## Slide 111: Displaying the Serial Monitor

## Slide 112: A Tour of the Serial Monitor

## Slide 113: A Tour of the Serial Monitor

## Slide 114: A Tour of the Serial Monitor

## Slide 115: A Tour of the Serial Monitor

## Slide 116: A Tour of the Serial Monitor

## Slide 117: A Tour of the Serial Monitor

## Slide 118: Baud Rate
How do we know how many 0’s and 1’s there are?
We tell how the computer and microcontroller how long a signal has to be high or low to count as a 1 or a 0 by setting the baud rate
For our purposes it doesn’t really matter what the baud rate is, it’s just important that the microcontroller and computer agree!

## Slide 119: Serial Commands
Serial.begin(baud_rate);
ex: Serial.begin(9600);
Serial.print(“Text”);
Serial.print(variable);
Serial.println(“Text”);
Serial.println(variable);

## Slide 120: Ask Arduino - Code Review

## Slide 121: Serial Communication: Serial Debugging
void loop()
{
int xVar = 10;
Serial.print ( “Variable xVar is “ ) ;
Serial.println ( xVar ) ;
}

## Slide 122: Serial Communication: Serial Troubleshooting
void loop ( )
{
Serial.print (“Digital pin 9: “);
Serial.println (digitalRead(9));
}

## Slide 123: Night Light - Code Review

## Slide 124: Analog Sensors
Examples:
Sensors | Variables
Photoresistor | light_level
Microphone | sound_volume
Temp Sensor | temp
Flex Sensor | bend
Accelerometer | tilt, acceleration

## Slide 125: Trimpot (Potentiometer) Variable Resistor
wiper
fixed
end
fixed
end

## Slide 126: Trimpot (Potentiometer) Variable Resistor

## Slide 127: Trimpot (Potentiometer) What does it mean?
Since we’re controlling the size of both bunnies:
We can make either bunny so small it gets zero carrots
We get the full range of 0-1023!
  This makes potentiometers excellent controllers for physical computing “settings”
  Can we think of any examples?
  But what if the setting we want to control has less (or more) than 1023 values? Or if we want it not to start at 0?
    Do math

## Slide 128: Trimpot (Potentiometer) What does it mean?
Since we’re controlling the size of both bunnies:
We can make either bunny so small it gets zero carrots
We get the full range of 0-1023!
  This makes potentiometers excellent controllers for physical computing “settings”
  Can we think of any examples?
  But what if the setting we want to control has less (or more) than 1023 values? Or if we want it not to start at 0?
    Do math
    Get the microcontroller to do it for us

## Slide 129: Map Command
int new_var = map(old_var, old_low, old_high, new_low, new_high);
ex: offset_val = map(val, 0, 100, -50, 50);
ex: reverse_val = map(val, 1, 100, 100, 1);
ex: write_val = map(read_val, 0, 1023, 0, 255);

## Slide 130
Project #5 – Real Time Color Mixer
Tying it all together...
Psuedo-code – how should this work?
Button A Pressed?
YES
Current LED?
BLUE
RED
Change to green
Change to red
Pressed Before?
NO
Change to blue
GREEN
Light green LED
Light yellow LED
Light red LED
Button B Pressed?
YES
Current LED?
BLUE
RED
Write a scaled trimpot value to red pin of RGB LED
Write a scaled trimpot value to blue pin of RGB LED
Read trimpot
Write a scaled trimpot value to green pin of RGB LED
GREEN

## Slide 131
Project #5 – Inputs and Outputs
Inputs | Outputs
a “Select” Button | Red Indicator
an “Adjust” Button | Green Indicator
Trimpot | Blue Indicator
 | RGB LED

## Slide 132: Project #5 – Real Time Color Mixer Schematic

## Slide 133: Project #5 – Real Time Color Mixer Wiring Diagram

## Slide 134: Where To Go From Here:

## Slide 135: Special Thanks:
www.sparkfun.com
6175 Longbow Drive, Suite 200
Boulder, Colorado 80301